1. Spectrum of slide/string noise
  1. Mute transverse vibrations
    1. Ear plugs
    2. Foam
    3. Tape
    4. Keeping the slide in contact the whole time
      1. Damping might kill longitudinal vibrations
      2. Put foam underneath the strings as a potential way
  2. Slide slide along the string and capture sound
    1. Attempt to maintain constant velocity
    2. Put things in place to limit length of string traveled
    3. Extract velocity based on timing from recording?
  3. Do unwound strings have longitudinal modes?
  4. Method
    1. Set metronome to 100 bpm to provide a consistent pulse
    2. Travel travel the following distances each beat for a measure of 4/4 (so they appear twice in succession)
      1. frets 5-7 one beat, frets 7-5 next beat
      2. frets 5-9 one beat, frets 9-5 next beat
      3. frets 5-12 one beat, frets 12-5 next beat
    3. Aim is to have different speeds in a manner which is as controllable as possible considering it is a human performing the test
2. Decay rate of a single winding/slide collision
  1. Use exacto knife to provide stimuli
  2. Muting
    1. Mute other strings with ear plugs/foam
    2. Mute transverse vibrations with left hand/foam (to minimize string distortions)
  3. Press thumb into blade of extaco to make it more rigid and easier to transfer motion into string windings
  4. Make several attempts in a recording to isolate one
  5. Methods
    1. Both rely on assumption of linearity
    2. Hold and Release
      1. Apply force with exacto knife in between windings
      2. Allow exacto to slip to release string and start motion
      3. More likely a measure of T60
      4. Less like an ideal impulse (especially considering initial conditions)
    3. Striking
      1. Drag exacto across ridges to strike a few windings
      2. Extract T60 value from the last decay
      3. Assumes T60 is sufficient to not have overlap between successive winding strikes